## Slide 1: Repurposable Devices and Tock
Tock World 5
July 19, 2022
Brad Campbell – bradjc@virginia.edu

## Slide 2: Repurposable IoT Devices
Devices designed today with new abstractions and architectures to enable longevity and utility commensurate with the physical hardware itself
Why?
IoT devices hard to deploy  want them to keep working for decades
E-waste is a growing concern, hard to recycle small IoT devices
Use cases change  want to update devices
100 years
~3 years
?? years

## Slide 3: Long-lived device challenges
Energy availability
  Harvesting required
  Energy conditions change over time
Use case changes
  Applications 10 years from now different than today
Moore’s law never really ended
  Tomorrow’s software written for tomorrow’s hardware
  Deployed devices use today’s hardware

## Slide 4: Opportunity for Tock & Repurposable Devices
Prerequisite: decouple apps from hardware and system management
  Syscall interface enables this
Enabling:
  Threat model
  Trusted apps (AppID)
  Robust cryptography APIs
RL-based Power Supply
Tock Operating System
App
App
Energy-Harvesting IoT Device
Crypto
App

## Slide 5: Application loading
Goal: dynamically add and execute new apps
Stages
Design space
  Where should app loading mechanism live in Tock?
  Current approach:
    As much as possible in userspace
    Capsule facilitates writing flash
    Core kernel approves new app, adds to queue, and executes
Tock
Userspace Loader
App
Core Kernel
Capsules
Application Loading

## Slide 6: OTA implementation for Tock
Prototype: OTA app runs in userspace
  First version used hardcoded addresses
nonvolatile_storage
nonvolatile_storage_driver
Component Layer
Capsule Layer
OTA
App Layer
System Call Interface
Flash Memory
Hardware Layer
Need to be changed according to the size of OTA app

## Slide 7: Load apps and update the PROCESSES array
Static
APP1
Grant 1
Process Control Block 1
APP2
Grant 2
Process Control Block 2
Kernel
App 1
App 2
App 3

## Slide 8: Current status: PR#3068
Feedback list of ‘pull request’
  Minimized the usage of ‘Unsafe’ in kernel module => Done! (use ‘Unsafe’ at core::slice::from_raw_parts / ProcessStandard::create / *self.ptr_process.offset(proc_data.index.try_into().unwrap()) = Some(process))
  Removed 3 Global variables (INDEX_OF_PROCESS / FLASH_START_ADDRESS / UNUSED_RAM_START_ADDRESS) => Done! (replaced by grant)
  Removed Hard code (#define) in OTA app => Done!
  Removed unnecessary code snippets (debug!(), test code, extern C..) => Done!
  Make CRC32(gh #3090) public to use it in process_load_utilities.rs => Done! (with the help of Alistair Francis)
  Need to transfer process_load_utilities.rs into capsule => To do?
Others
  Integrate ‘button version OTA app’ with ‘UART version OTA app’. For implementation test of OTA app, the button version OTA will be used
  Organized code (Python, process_load_utillties)
  Update the pull request??

## Slide 9: Will the updated device still work?
Risk: new combination of applications not harmonious on already deployed hardware
Testing architecture enables analyzing behavior of Tock platforms with new apps
  Architecture three key components
    Test monitor
    Energy meters
    Device under test
Device under test is any IoT device running the OS of interest
Software on the test monitor runs a workload on the IoT device
  Test monitor: Raspberry PI (~$50)
Device under test has communication channels back to the test monitor
Examples: test energy and memory
9
Test Monitor
Device under test
Energy Meters

## Slide 10: Testing software framework
Tests execute on the test monitor
Test framework:
  Loads tests to run
  Initializes the device under test
  Parses inputs from device and monitors energy, events, and state
  Compares observations to test requirements (pass/fail)
Tests are written in code, but compiled separately.
[software framework architecture diagram]

## Slide 11: Issue #1: Energy
Energy is a critical challenge in IoT devices
Storing or collecting energy typically dominates the size
Less energy consumption: longer device lifetime, less maintenance, overall lower cost of operation
Smartphones, for example, include energy tracking
Example questions:
  My IoT device is drawing too much power, but why?
  Will this change affect the power draw?
  Which OS uses less power?
MCU
Light Sensor
Motion Sensor
CO2 Sensor
Wireless Radio
Battery
LCD Screen
Typical IoT Device
Energy is consumed by each physical component on the device.
Notes: Assuming no visibility

## Slide 12: Running an energy test
Test monitor observes the energy consumption of each hardware component
Opaque: no modification or insight into OS
Energy test:
  Define the component to evaluate
  Set allowed energy bounds
  Run the device determine if conditions are met
EnergyTest::new( "radio-packet-tx", // test name "radio_send_app”, // test app
// test operations &[Operation::reset_device(), // reset Operation::idle_testbed(5000)], // wait 5s
&[Criterion::Energy(
EnergyCriterion::new(EnergyStat::Total) .with_max(350))] // max 350 mJ
)
Criterion (maximum limit)
Monitored trace
MCU
Light Sensor
Motion Sensor
CO2 Sensor
Wireless Radio
Battery
LCD Screen
Typical IoT Device
Test Monitor
Energy Meters
Device under test
Notes: Assuming no visibility

## Slide 13: Testing radio energy consumption
radio-packet-tx Complete (in 3.000016813s) Platform specification: Energy metering: system-total (5441 samples)=== Criteria summary: - Energy: 'system-total' max consumption
min: -
max: 120.00 mW) (Pass) Message: 112.24mJ/s max
Criterion (maximum limit)
Monitored trace
Test monitor runs the test, monitors the hardware, and evaluates the pass/fail criterion

## Slide 14: Issue #3: Memory
Embedded IoT devices have limited memory
  Typical: ~64 kB of RAM
  Comparison: Macbook Pro: 32 GB, Raspberry Pi: >2 GB
Memory is important!
  Memory bugs lead to security vulnerabilities
  SRAM is a major contributor to standby power draw
  Memory is fixed when a device is manufactured
  Re-engineering to reduce memory use is expensive
Large space to explore…
  Focus on application memory requirements
  Transparent: assume full access to modify Tock as needed

## Slide 15: Primer: In Tock, processes have a fixed RAM memory region
All process-specific kernel state is stored in the process’s allocated memory (in the “grant” region).
  That way, if a process requests too many resources only that process fails
Testing goal: enable testing process memory usage
  Modify kernel
  Unmodified processes
Data
Stack
Heap
Grant section
Timer1 allocation
BLE allocation
Data
Stack
Heap
Grant section
Timer1 allocation
Timer2 allocation
Timer3 allocation
Timer4 allocation
Timer5 allocation
Process RAM Allocation
Process 1
Process 2

## Slide 16: We modified Tock to create a counter table to account for all process memory
Counters track fine-grained process memory usage
Counters are updated every time memory usage changes
Device only streams updated counter values when they change
  Reduces communication overhead
Test monitor tracks memory usage over time
Data
Stack
Heap
Grant section
Timer1 allocation
BLE allocation
Metric | Size
Grant Header | 242 B
Grant Region | 1960 B
Stack Size | 116 B
In-kernel counters
Test Monitor
Device under test
UART

## Slide 17: Memory testing mechanism enables comparing versions of the operating system
August 2021: 2.0 release of Tock
Does 2.0 treat process memory differently?
  Need to know how OS version updates will affect application operation.
  Should we install the OS update now?
Tock version | process control block | upcall queue | grant pointer table | grant data | total
1.6 | 644B | 360B | 52B | 284B | 1340B
2.0 | 648B | 360B | 112B | 188B | 1308B

## Slide 18: We can also observe what effects hardware platforms have on process memory
Run same process on multiple hardware boards
Compare memory use
Example of top-down testing approach
Results
  2% memory overhead penalty based on per-hardware kernel configuration

## Slide 19: Memory test results
Test monitor tracks memory usage over time and evaluates conditions
Memory usage depends on application behavior over time

## Slide 20: Repurposable devices
Dynamic app loading and updates
Testing/debugging app and system changes
Managing the inevitable relative decay of hardware

## Slide 21: Simulate the future by downgrading the present
Consider in ten years…
  Embedded microcontrollers include a decade of improvements
  Software grows to fill hardware
    2012: Hacking to fit TinyOS + 6LoWPAN + UDP + RPL + Deluge on msp430f1611
    2022: Hacking to fit Tock on Ti50
Emulate future HW-SW divergence
  ./futurebuild -7y imix # compile imix for 7 year old hardware
  Adjust RAM and flash sizes based on trends
  Insert nops or adjust clock for slower/less performant HW
  Disable ISA extensions

## Slide 22: Upgrade the edge, not the devices
Future: ~1000:1 sensors to gateways
  Easier to upgrade one gateway than one thousand IoT devices
  Benefit from increased compute and new accelerators
Provision devices today to support app offload
  Essential tasks (sensing, low latency) remain on-device
  Computation shifts to gateways
Q: what abstractions needed for app developers?
Power Supply
Operating System
App
App
Shadow App
IoT Device
Edge Platform
App
Edge Gateways
App
Edge Offloading
…

## Slide 23: Questions?
Brad Campbell
bradjc@virginia.edu

## Slide 24
24
24
Hardware
CPU
I2C
SPI
RNG
UART
Timer
AES
ADC
DAC
Documented Interface
Processes
Scheduler
Wireless
MPU
Timer
ADC
Debug
Encryption
Sensor
Kernel (Rust)
Sense-and-send
Machine Learning Data Processing
Malicious! while(1)
😈